## Slide 1
Figure The time-domain and frequency-domain plots of a sine wave

## Slide 2
A complete sine wave in the time domain can be represented by:
One single spike in the frequency domain.

## Slide 3
The frequency domain is more compact and useful :
When dealing with more than one sine wave.
Example

## Slide 4
Figure The time domain and frequency domain of three sine waves

## Slide 5
Single-frequency sine wave is not useful in:
Data communications.
Need to send a composite signal:
Signal made of many simple sine waves.

## Slide 6
According to Fourier analysis, any composite signal:
Combination of simple sine waves.
Have different frequencies, amplitudes, and phases.

## Slide 7
If the composite signal is periodic.
  Decomposition gives a series of signals with discrete frequencies.
If the composite signal is nonperiodic.
  Decomposition gives a combination of:
  sine waves with continuous frequencies.

## Slide 8
Figure A composite periodic signal

## Slide 9
Figure Decomposition of a composite periodic signal in the time and frequency domains

## Slide 10
Figure The time and frequency domains of a nonperiodic signal

## Slide 11
Bandwidth of a composite signal is the difference between:
Highest and the lowest frequencies

## Slide 12
Figure The bandwidth of periodic and nonperiodic composite signals

## Slide 13
If a periodic signal is decomposed into five sine waves with frequencies
  100, 300, 500, 700, and 900 Hz
  What is its bandwidth?
Draw the spectrum, assuming all components have a maximum amplitude of 10 V.
Example

## Slide 15
Figure The bandwidth for Example

## Slide 16
A periodic signal has a bandwidth of 20 Hz.
The highest frequency is 60 Hz.
What is the lowest frequency?
60 Hz
20 HZ
40 Hz
80 Hz

## Slide 17
Draw the spectrum if the signal contains all frequencies of the same amplitude.

## Slide 18
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Example

## Slide 19
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure shows the frequency domain and the bandwidth.

## Slide 20
Figure The bandwidth for Example

## Slide 21
DIGITAL SIGNALS
  Information can also be represented by a digital signal.
For example
1 can be encoded as a positive voltage and a 0 as zero voltage.
A digital signal can have more than two levels.
In this case, we can send more than 1 bit for each level.

## Slide 22
Figure Two digital signals: one with two signal levels and the other with four signal levels

## Slide 23
A digital signal has eight levels.
How many bits are needed per level?
16
3
8
0

## Slide 24
Ans B

## Slide 25: Bit Rate
Most Digital Signals are non-periodic.
  Therefore, period and frequency are not appropriate characteristics.
Bit rate is used.
Bit rate is number of bits sent in 1s. Expressed in bps.

## Slide 26
A digitized voice channel is made by digitizing a 4-kHz bandwidth analog voice signal.
We need to sample the signal at twice the highest frequency (two samples per hertz).
We assume that each sample requires 8 bits. What is the required bit rate?
64 kbps
12 kbps
32 kbps

## Slide 27
The bit rate can be calculated as

## Slide 28: Bit Length
Bit length:
Distance one bit occupies on transmission medium.
Bit length= propagation speed* bit duration

## Slide 29
Figure Baseband transmission
Notes: transmit a digital signal by using one of two different approaches: baseband transmission or broadband transmission
Baseband transmission means sending a digital signal over a channel without changing
the digital signal to an analog signal

## Slide 30
A digital signal is a composite analog signal with:
An infinite bandwidth.
Note

## Slide 31
Figure Bandwidths of two low-pass channels
Notes: Low-Pass Channel with Wide Bandwidth
If we want to preserve the exact form of a nonperiodic digital signal with vertical segments vertical and horizontal segments horizontal, we need to send the entire spectrum, the continuous range of frequencies between zero and infinity.

## Slide 32
Baseband transmission of a digital signal that:
Preserves the shape of the digital signal
This is possible only if :
Have a low-pass channel with an infinite
or
very wide bandwidth.

## Slide 33
In baseband transmission:
Required bandwidth is proportional to the bit rate
If need to send bits faster, need more bandwidth.
Bit rate is twice the bandwidth required.

## Slide 34
What is the required bandwidth of a low-pass channel?
If we need to send 1 Mbps by using baseband transmission?
Example

## Slide 35
What is the required bandwidth of a low-pass channel if we need to send 1 Mbps by using baseband transmission?
Solution
The minimum bandwidth, is B = bit rate /2, or 500 kHz.
Example

## Slide 36
We have a low-pass channel with bandwidth 100 kHz.
What is the maximum bit rate of this channel?
100 kbps
200 kbps
400 kbps
Example

## Slide 37
Broadband Transmission: Bandwidth of a bandpass channel

## Slide 38
If the available channel is a bandpass channel:
  Cannot send the digital signal directly to the channel
Need to convert:
Digital signal to an analog signal before transmission.

## Slide 39
Figure Modulation of a digital signal for transmission on a bandpass channel

## Slide 40
An example of broadband transmission using modulation is
Sending of computer data through a telephone subscriber line
Example

## Slide 41
🌊 Oh no! To cross this river
(and save your data from leaking 💦),
match the tech-terms with their true powers!
🔹 Column A
- Bit rate
- Bit length
- Digital
- Baseband BW
🔹 Column B
- Speed of bits in 1s 🕐💨
- Space each bit takes 🛏️
- Goes on forever like bedtime stories 📖♾️
- Grows with bit speed 🚀📶
Notes: Puzzle 1 Answers:
- Bit rate → Speed of bits in 1s
- Bit length → Space each bit takes
- Digital → Goes on forever like bedtime stories (infinite bandwidth)
- Baseband BW → Grows with bit speed
Justification:
Bit rate = bits per second; Bit length = physical distance of one bit.
Digital signals theoretically have infinite bandwidth.
Baseband bandwidth increases with bit rate (BW = bit rate / 2).

## Slide 42
🚣‍♂️ Another river!
This time it's filled with sine
waves and spikes.
Match the terms to stay dry!
🔹 Column A
- Fourier
- Composite
- Freq. Dom
- Bandwidth
🔹 Column B
- Turns waves into tiny beats 🎧
- Group of wave friends 🎊
- Spiky signal spectrum 🌊📊
- Highest minus lowest note 🎼📏
Notes: Puzzle 2 Answers:
- Fourier → Turns waves into tiny beats
- Composite → Group of wave friends (sine mix)
- Freq. Dom → Spiky signal spectrum (frequency view)
- Bandwidth → Highest minus lowest note (range)
Justification:
Fourier: analysis technique to break signal into sine waves.
Composite: combination of multiple sine waves.
Frequency domain: represents sine components as spikes.
Bandwidth: frequency range = f_high - f_low.